## Slide 1: Unrolling the shutter: CNN to correct motion distortions
Vijay Rengarajan, Yogesh Balaji, A.N. Rajagopalan
Indian Institute of Technology Madras
Image Processing and Computer Vision lab, Department of Electrical Engineering, IIT Madras

## Slide 2: Camera Motion Causes Rolling Shutter Distortions
Mobile phones
Drone cameras
Streetview capture
Motion blur
Lens distortions

## Slide 3: Sequential Exposure of Rolling Shutter
0
time
Global shutter CCD image sensor
Exposure close
Exposure open
Exposure time
te
0
Top row
Bottom row
time
Td
Total line delay
te
Top row
Bottom row
All pixels expose at the same time
Rolling shutter CMOS image sensor
Each row starts exposing sequentially

## Slide 4: Rolling Shutter Distortions are Geometric
Different rows see the scene at different poses of the moving camera
Even short exposure causes distortions
x
z
y
x
z
y
tx translation
rz rotation
Scene
Captured image
Scene
Captured image
time
time

## Slide 5: Correct Rolling Shutter Distortions from a Single Image
Disturbs visual appeal
Affects scene inference
Single image ambiguity
curved building or rolling shutter effect?

## Slide 6: Prior Works on Rolling Shutter Correction
Rengarajan et al. CVPR (2016) for urban scenes
Heflin et al. Conf. Biometrics (2010) for faces
Rolling shutter
Curvatures
Corrected
Rolling shutter
Corrected using facial features
Ringaby and Forssen
CVPR (2010)
IJCV (2012)
Grundmann et al.
ICCP (2012)
Video rolling shutter correction
Use frame-to-frame point correspondences
Need
A single method that can be used for different classes of images
Different levels of features to correct extract motion and to discard feature outliers

## Slide 7: Let machines extract desired features
Convolutional Neural Network
Input Rolling shutter image 256x256x3
Output Translation and rotation (tx,rz)
15 tx and 15 rz motion samples of
equally spaced rows
Train for different classes of images
Motion Fitting
Distortion Correction
Corrected Image
Rolling shutter distorted image
CNN
Feature Extraction
Motion Estimation
Distortion Correction
Corrected Image
Rolling shutter distorted image
Existing approach
Motion fitting
Polynomial trajectory to get tx and rz for each row
Distortion correction
Inverse warping based on row-wise motion
1
2
3

## Slide 8: VanillaCNN with square filters
Vanilla Convolutional Neural Network
Motion Mean Squared Error
tx and rz at 15 rows
VanillaCNN
Translations only
Translations and rotations
Corrected by
VanillaCNN
Distorted image
Distorted image
Corrected by
VanillaCNN
1
2

## Slide 9: Ideas for a new architecture
Initial feature extraction
Feature combination
Any better ideas?
Along rows : motion constancy
Along columns : temporal motion
Notes: Rotation can be better estimated if information from image rows are extracted earlier

## Slide 10: Use long filters for RowColCNN
Motion Mean Squared Error
Captures information in rows early
Captures information along time dimension early
Filter h x w x c

## Slide 11: Use long filters for RowColCNN
Motion Mean Squared Error
Captures information along row dimension early
Captures information along time dimension early
    Training Data Generation
      Generate random polynomial camera trajectory
      Apply on undistorted image
    Correction
      Get camera motion values from CNN
      Fit a polynomial trajectory and get motion at all rows
      Correct distorted image using target-to-source mapping
    Datasets
      Chessboard Urban scenes Faces
      7k 300k 250k
      Sun Oxford Zurich LFW
Corrected by
VanillaCNN
Corrected by
RowColCNN
Notes: The datasets do not have rolling shutter effect. We synthetically generate them. Even so, it works for real images that we captured using mobile phones.

## Slide 12: Correction Results of RowColCNN

## Slide 13: Learning excels in challenging conditions
Geometry-based
Learning-based
Distorted input
Rengarajan et al. (2016) fail due to tree branches which are naturally curved
Heflin et al. 2010
RowColCNN
RowColCNN
Rengarajan et al. 2016
Heflin et al. (2010) fail due to wrong estimation of facial features in varied illumination conditions

## Slide 14: New CNN filter shapes inspired by application
New learning-based method for single image rolling shutter correction
CNN learns image to motion mapping
Long filters in CNN architecture for rolling shutter exposure
apvijay.github.io/rs_rect_cnn
Poster 21 AM