## Slide 1: Non-local Means Filtering
EE5175 Image Signal Processing

## Slide 2: Mean filtering
Each output pixel is the average of intensities present in a neighbourhood around the corresponding input pixel
Box function
Normalization
acts as averaging here

## Slide 3: Mean filtering
depends only on the pixel location
Takes into account all pixels q which are inside a box radius with p as centre
Choose q only within W-box radius around p

## Slide 4: Mean filtering
Box radius
Box dimensions
All ones filter (before normalizing)

## Slide 5: Gaussian filtering
Each output pixel is the Gaussian weighted average of intensities centred around the corresponding input pixel
Gaussian weighting
Normalization

## Slide 6: Gaussian filtering
Each output pixel is the Gaussian weighted average of intensities present in a neighbourhood around the corresponding input pixel
Choose q only within W-box radius around p
Weight based on spatial distance between p and q

## Slide 7: Gaussian filtering
Box radius
Box dimensions
Gaussian filter

## Slide 8: Mean and Gaussian filters
Operate in the same manner irrespective of image intensities
Only depend on spatial locations around a pixel
Cause space invariant blur
  Useful to model optical lens blur (defocus blur)
Bad for applications such as denoising
  Do not care about edges

## Slide 9: Denoising additive Gaussian noise
Noisy image
Mean filter
Gaussian filter

## Slide 10: Non-local means (NLM) filter
Averages pixels that have similar neighbourhoods
If neighbourhood of p looks similar to neighbourhood of q, give higher weight
The weight depends on image intensities
Gaussian weighting based on difference in image intensities
Normalization

## Slide 11: Non-local means (NLM) filter
Weighs neighbour pixels that have similar neighbourhoods
Similarity weight based on intensities of neighbourhood around p and q
Choose q only within W-box radius around p

## Slide 12: Non-local means (NLM) filter
Higher weight
looks similar to p
Lower weight
Similarity neighbourhood
Search neighbourhood
If W covers the whole image, then each output pixel depends on input pixels at any location “non-local”

## Slide 13: Non-local means (NLM) filter
A
B
A
B
Mean and Gaussian filtering
  Filters (kernels) at A and B are same
  Convolution can be used
Non local means filtering
  Filters (kernels) at A and B are different
  Convolution cannot be used

## Slide 14: Non-local means (NLM) filter
Operates based on image intensities
Specifically, based on image neighbourhood around a pixel
Causes space variant blur
Good for applications such as denoising
  Preserves edges

## Slide 15: Denoising
Noisy image
Mean filter
Gaussian filter
Non local means filter